## Slide 1: How does an antenna that only generates a magnetic field, generate an electromagnetic (EM) wave?

## Slide 2
Made up of two time varying components:
  Electric field (E)
  Magnetic field (B)
Electric and magnetic fields
  Orthogonal and in phase
  Are tightly coupled to each other
  Propagate through space at the speed of light
  How do we know this: Maxwell’ equations
Greatest physicists all time:
  Newton (F= ma)
  Einstein (E= mc2)
  ?
Electromagnetic (EM) Wave

## Slide 3
Electromagnetic (EM) Wave
Made up of two time varying components:
  Electric field (E)
  Magnetic field (B)
Electric and magnetic fields
  Orthogonal and in phase
  Are tightly coupled to each other
  Propagate through space at the speed of light
  How do we know this: Maxwell’ equations
Greatest physicists all time:
  Newton (F= ma)
  Einstein (E= mc2)
  Maxwell (Maxwell’s equations)

## Slide 4
Force Fields & EM Waves
Charged particle: free electron (which has a negative charge)
Constant electric field is produced by a stationary charged particle
  Example: a capacitor with a DC charge
Constant magnetic field is produced by a moving charged
  Important point: charges are moving at a constant velocity
  Example: a DC current flowing thru a conductor
An EM wave is produced by an accelerating charged particle
  Examples:
    Particle accelerator
    AC current flowing thru a conductor of sufficient length

## Slide 6
Why Are Maxwell’s Equations Important
Show the link between electricity, magnetism and light
  Show that light is a form of EM radiation
Break down under some conditions
  Led Einstein to Theory of Relativity
Mathematical description of how EM waves are generated and altered

## Slide 7
How Does An EM Wave Get Generated
From Maxwell’s equations:
  A time varying electric field induces a time varying magnetic field
  A time varying magnetic field induces a time varying electric field
  This interplay between induced electric and induced magnetic fields leads to propagating electromagnetic waves
Most antennas do not launch an EM wave
  They generate either a time varying electric field or a time varying magnetic field

## Slide 8
Spatial Fields (Distance From An Antenna)
Pure EM waves only exist in the Far Field

## Slide 9
Spatial Fields (Distance From An Antenna)
Pure EM waves only exist in the Far Field
MHz | 
3.5 | 175 ft
144 | 4.3 ft
564 ft
14 ft

## Slide 10
EM Wave From A Magnetic Field Generator
Reactive
Near-field
Conductor length must be > 0.05 wavelength to radiate
(LC tank circuits don’t radiate because they are << 0.05 wavelength)
  Initially:
  E & B fields are orthogonal but 90o out of phase
  Energy goes back and forth between E & B fields
  No radiation
  Analogous to a lossless LC tank circuit

## Slide 11
EM Wave From A Magnetic Field Generator
Radiating
Near Field
Length must be > 0.05 wavelength to start radiating
(This is why LC tank circuits don’t radiate)
(Transition region)
Reactive
Near-field

## Slide 12: EM Wave From A Magnetic Field Generator
Far Field
Length must be > 0.05 wavelength to start radiating
(This is why LC tank circuits don’t radiate)
  E & B fields in-phase
  Full radiation
  No reactive energy

## Slide 13
Magnetic Loop Antenna
Reactive
Near-field
RF
Far Field Pattern

## Slide 14
Electric Field Antenna
DC
+
-
E Field

## Slide 15
Electric Field Antenna
DC
+
-
E Field
=>
RF
+
-
E Field
=>
L/2
L/2
L> 0.05 wavelength
Reactive
Near-field

## Slide 16
Magnetic Loop Antenna
Why is it called a Magnetic Loop antenna?
  In the reactive near-field:
    It generates a magnetic field on transmit and,
    It responds primarily to the magnetic field of an EM wave when receiving
In the far field, there is no difference between the EM wave generated from a magnetic loop or from a dipole
Ground effects:
  Near field: detuning and losses are minimal
  Far field: similar to ground mounted vertical
Pseudo-Brewster angle notch-out